## Slide 1
Use this Alert: Discuss in Tool Box Talks and HSE Meetings  Distribute to contractors  Post on HSE Notice Boards  Include in site HSE Induction
Contact: MSE54 for further information or visit the HSE Website Learning No14 31/03/2014
PDO Safety Advice
Date: 31/03/2014
Derrick Man surfing Leg and Hand fracture
What happened?
A Derrick Man struck by a rotating pony rod bar which was left on a Mud Pump after maintenance.
Your learning from this incident…
Ensure work areas are safe prior to start the operation.
Ensure lock out & tag out system is implemented by applying 3 padlocks
Always make sure that Original Equipment Manufacturer (OEM) tool is used to rotate the pony rod bar and Never use/accept home made tools.
Ensure that sufficient light is available in work areas
Always make sure that pony rod bar is removed prior to operate the mud pump
Do not de-isolate mud pump until pony rod bar removed and all safety precautions are taken
One Pad-Lock
Must be 3 Pad-Lock

## Slide 2
Contact: MSE54 for further information or visit the HSE Website Learning No14 31/03/2014
Management learning's
Date: 31/03/2014
Derrick Man surfing Leg and Hand fracture
As a learning from this incident and ensure continual improvement all contract
managers are to review their HSE HEMP against the questions asked below
Confirm the following:
Do you have requirement to inspect the work site on completion of the job?
Do you have isolator available in night shift?
Are junior mechanic / elect are aware about PTW & LOTO requirement?
Do you ensure that task relevant Job Safety Analysis (JSA) / Drilling Operation Procedure (DOP) are communicated to all involved personnel?
Do you have a system to ensure actions from lateral Learnings are implemented?.
Is the alert/learning advice understood by the crew members?.
Use this Alert: Distribute to contractors  HSE Meetings