## Slide 1
Use this Alert: Discuss in Tool Box Talks and HSE Meetings  Distribute to contractors  Post on HSE Notice Boards  Include in site HSE Induction
Contact: MSE54 for further information or visit the HSE Website Learning No13 28/12/2013
PDO Safety Advice
Date:28/12/2013
Incident: Gas Leak
What happened?
A hydrocarbon gas leak occurred at a cross over connecting the coiled tube lubricator with the quick test sub. As the 1.75’’ coil tubing was already at the surface the CIRP stacks were activated and manually locked and the two 7/8’’ guns were situated across the BOP so it could not be used. The leak lasted for 20 minutes until TRSSSV in the well was closed to stop the leak.
Your learning from this incident..
Issue PTW only when a full JSA is complete and all required controls are in place.
Before starting a job ensure everyone understands the applicable emergency response procedure.
Know your barriers before starting any well intervention

## Slide 2
Contact: MSE54 for further information or visit the HSE Website Learning No13 28/12/2013
Management learning's
Date:28/12/2013
Incident: Gas Leak
As a learning from this incident and ensure continual improvement all contract
managers are to review their HSE HEMP against the questions asked below:
Confirm the following:
Do well test and TCP supervisors attend IWCF for CT and W/L?
Do you conduct pre-job engagement with all stakeholders prior any critical job?
Do you have OEM certificates for all equipment you use on site?
Do you have emergency response plans for different scenarios?
Do you have a system to ensure actions from lateral Learnings are implemented?
Is the alert/learning advice understood by the crew members?
Use this Alert: Distribute to contractors  Discuss in Meetings