## Slide 1: Reducing the risk of groundwater contamination by spilled oil-Case Study
Zahran Al-Busaidi

## Slide 2: Table of Content
Overview
The Incident
Location
Geology of the Area
Spill Response
Cleanup / Remediation
Social Challenges
Monitoring

## Slide 3: Overview
Petroleum Development Oman (PDO) is the major exploration and production company in the Sultanate of Oman.
Its hydrocarbons production in excess of one million barrels of oil equivalent per day.
It accounts for more than 70% of the country's crude-oil production and most of its natural gas supply.
Operates an area of about 100,000 km2.
Established 7,500 km pipelines and 12,000 km flowlines connecting 56 stations.
Operates the main oil line which crosses the desert, passing through wadis and nearby villages until Muscat.

## Slide 4: The Incident
On 8th April 2008, the Block Valve Station 6 (BVS6) of 38” Main Oil Line (MOL) leaked near the Bidbid village, 60km from Muscat.
Oil export from the North and South main oil line was stopped from Fahud and Qarn Alam.
Stopped the MOL pumping stations.
Closed the upstream BVSs remotely.
PDO Emergency Response Team was mobilised immediately.
The leak was at the flanged fittings, pressure gauges and pressure transmitter.
Stopped the leak on 20” flange by closing the local isolation valves.

## Slide 5: Initial Photographs of the Spill
Source of Leak- 20” Blind flange

## Slide 6: Spill Location
Satellite map showing BVS 06 and the main pipeline to MAF
BVS 06
MAF
2km
N

## Slide 7: Spill Site Conceptual Sketch

## Slide 8: Initial Response
Informed the Ministry of Environment about the incident.
Various contractors were deployed to the site.
Clean up of site started.
Conducted a geological and Hydrogeological study.
Conducted an Environmental Impact Assessment Study.
An Environmental consultant was appointed to monitor the environmental performance and prepare progress reports.
Site control was done to manage contractors (160 people, 30 machinery) day and night.
Wali, local Citizens, Shareholders, Management and various concerned government firms, were kept informed of the cleanup progress.

## Slide 9: Spill in a Geologically Complex Area
Spill in a wadi (valley) showing the mini-channels followed by oil stream(s). The oil channels are more winding and spread upstream making the excavation process more challenging in this part.

## Slide 10: Geological overview of the area
Schematic 3D representation of the Spill Wadi with different recent alluviums (wadi gravel) accumulations and relatively shallow water level of the bank storage.

## Slide 11
Old Alluviums
Harzburgite
Harzburgite (ophiolite) in contact with old alluvial (conglomerate)
An old Alluvium fracture in which oil has migrated through.
Fault and Fracture systems
Fractures are within the old Alluviums (conglomerate) and do not penetrate through the Harzburgite.
Oil migrated through some of the fractures (but restricted within the area).
The fractures are restricted in small zones.
Old Alluviums
Oil stains within the rocks

## Slide 12: Spill Cleanup
Surface cleanup and excavation started.
Absorbent was utilized to contain any oil in surface water.
Pits and trenches excavated to contain any seepage of oil down-gradient.
Oily water pumping out on a continuous basis to prevent re-establishment of normal down gradient groundwater flow.
Cutting of trenches down to at least 0.5m below water table in the fresh bed rock section and about 1metre wide at marked locations should commence.
Chemical cleaning of oil from rocks and rock surfaces.
Water and air jet cleaning was practiced.

## Slide 13: Spill Cleanup

## Slide 14: Cleanup
High Pressure Flushing of rocks
Oil recovery and contaminated soil removal

## Slide 15: Main Wadi Protection
Absorbent sheets were kept to collect any oil reaching the wadi entrance
Entrance of the water channel protected using booms

## Slide 16: Social Challenges
Access
Water Supply
Compensation
Health Complaints

## Slide 17: Social Management
Meetings were held with the tripes representatives to explain the progress of the cleanup.
Various social projects were done on the area.
Health and Social Impacts evaluation was done.
Water Monitoring programme was done.

## Slide 18: Environmental Monitoring
Seven monitoring wells were drilled, with pumping capability (wider wells).
Short, medium and long term groundwater monitoring plan was put in place.
Analyse for BTEX, initially every months, then every 3 months (once the BTEX was in the drinking water standard) and finally every year.

## Slide 19: Remediation Completion
Site cleanup and restoration commenced in 2008 and was completed in 2010.
By end of 2010, the site was declared clean and monitoring continued.
Since then the water was within the drinking water standard.
Groundwater monitoring continued regularly.

## Slide 20: The END

## Slide 21: Backup Slides

## Slide 22: Geology of Oman
Oman has vast geology that runs 100s of Millions years.
Sea of Oman
Emplacement of the Hawasina and Semail nappes from Hanna, 1995.

## Slide 23: Ways to prevent spills
Double Layer Tank
Pressure relieve valve
Secondary containment
Blowout preventer.
Suitable design of the primary storage.
Integrity checking/inspection.

## Slide 24: Secondary Containment
Note:
For illustration purpose only.
High spill potential (e.g. main oil line’s block valve stations, tank farm) shall be constructed in a bund appropriately designed, impervious and compatible with the material stored in it.
The bunded area shall not be less than 110% of the largest container in the system or 25% of the aggregate total capacity of the containers, whichever is the greater.

## Slide 25: Source-Pathway-Receptor
Conceptual models present the hypothesised relationships between:
  the source (S) of a hazard,
  the pathways (P) by which exposure might occur, and
  the receptors (R) – those features of the environment that we value and that could be harmed (S-P-R).
Hazard | Source | Pathway | Receptor
Crude Oil | Pipeline | Leaching Groundwater Supply | Farms People Animals

## Slide 26: Conceptual Site Model
Source: Public Health Assessment Guidance (ATSDR 2005)

## Slide 27: CSM for Petroleum release
Source: Management and remediation of sites in the petroleum industry, IPECA, 2014

## Slide 28: Risk Based Corrective Actions
RBCA: Risk Based Corrective Actions.
Source: Shell International B.V., The Hague, the Netherlands

## Slide 29: Sustainability Indicators for Remediation
After SuRF-UK, March 2010).
The table below gives an overarching categories of indicators for sustainability assessment of remediation
Environmental | Social | Economic
Impacts on air (including climate change) | Impacts on human health and safety | Direct economic cost and benefits.
Impacts on soil | Ethical and equity considerations. | Indirect economic costs and benefits.
Impacts on water | Impacts on neighborhoods or regions. | Employment and capital gain.
Impacts on ecology | Community Involvement and Satisfaction. | Gearing.
Use of natural resources and generation of wastes. | Compliance with policy objectives and strategies. | Life-span and “project risks”
Intrusiveness | Uncertainty and evidence. | Project flexibility.

## Slide 30
Data Evaluation &
Hazard Identification
Exposure Assessment
Toxicity Assessment
Risk Characterization
Identification of potential exposure scenarios and receptors.
Determine receptor specific exposure parameters, constituent-specific exposure parameters, and quantification of potential exposures.
Identification of toxicity values (carcinogenic and non-carcinogenic toxicity assessment).
Selection of toxicity factor.
Carcinogenic risk characterization.
Non-carcinogenic ri
sk characterization.
Risk characterization results for each receptor.
Health Risk Assessment
Identification of Constituents of Potential Concern
Source: ENSR Environmental International, Inc. (2005)

## Slide 31: Social Impacts Management
Know your stakeholders/ affected parties:
  Neighbors
  Local Ministry/government office
  Central Ministries
  Watch groups (e.g. Green Peace).
  Shareholders.
  Employees.

## Slide 32: Social Impact Management
2. Gain trust and respect by affected parties.
  Be transparent.
  Be active and serious in taking a remedial action.
  Be diplomatic.
  Compensate affected party.
  Monitor social, health and environmental impacts.
  Put and execute a suitable plan to manage social, health and environmental impacts.
  Keep consulting locals throughout the project phases.
  Keep all concerned parties informed.

## Slide 33: Risk Management Strategies
1. Source Removal/Treatment:
Removal or treatment of secondary source materials (i.e. affected soils, sediments, groundwater, etc.) so as to remove or reduce concentrations of contaminants to levels equal to or below the applicable remediation goals. Examples include:
Excavation. | Pump and treat.
Soil venting. | Biological action.

## Slide 34: Risk Management Strategies
Capping, | Barrier walls,
Building design, | Soil stabilisation,
Hydraulic containment | Natural attenuation
2. Containment Measures:
Long-term engineering controls to prevent migration of harmful concentrations of contaminants from the source to the points of exposure. Examples include:

## Slide 35: Risk Management Strategies
3. Institutional Controls:
Legal or administrative measures to control the nature and/or frequency of contact at the point of exposure. Examples include:
Land use restrictions. | Alternative water supply.
Personal protective equipment. | Permit requirements.

## Slide 36: Location Map