## Slide 1: Learning From Incident Awareness Alert
Target audience for this alert
Construction, Drilling, Operations ,Engineering, Exploration, Project and Logistic.
Description of the incident:
A crew was offloading palletized wooden boxes out of the 40-foot container loaded on a flatbed truck. In absence of the right machine, the crew decided to use a regular forklift and synthetic web slings to drag the boxes out of the container where one end of the sling was attached to the forklift mast and the other end was looped around blocks at the bottom of the wooden pallets. After offloading 5 boxes, the crew decided to drag the last 2 palletized boxes together at the same time. At this point, the flagman was standing outside of the truck and in close proximity (1.5m) from the back end of the flatbed trailer. As the forklift backed up and the boxes moved for about 2m, the blocks on the pallets got dislodged under tension, propelled towards the forklift and struck the flagman in the head.
Alert NO | External Alert _OQ _0121102020 | Pattern | Lifting
Date | 29th September 2020 | Directorate | ----------------------------
Notes: Target audience for this alert
List the position names or roles that are the target audience for this alert. Wherever possible, the target audience should be limited to those in positions or roles or locations for which the lesson learnt are relevant, or who are required to take action upon receiving this Alert.
Position or role name
Position or role name
Description of the incident:
This should be free text writing and include the relevant facts explaining. what happened to all the relevant parties in a short sharp factual paragraph that describes the incident.
Without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more
The description should be in sufficient detail to allow a person who does not know anything about the incident to imagine it.
It should only be about what happened and not why it happened.
DO NOT include investigation findings here, simply describe the incident as the investigation has shown it happened.
DO NOT give us a sequence of events here.

## Slide 2: Learning From Incident Awareness Alert
Why it happened:
Attempting to pull two pallets by the pallet blocks on the leading edge using a forklift which would only be held in by the securing nails.
Lessons learned:
Ensure the lift plan and the risk assessment are in place.
Ensure follow a proper method to load/off load pallets.
Pallets are designed to be lifted and, they are not designed to be pulled along the ground.
Ensure all participants are way from the line of fire.
Ensure the equipment being used is appropriate for the job.
Ensure the work area is clear before carrying out the operation.
Ensure that people are competent for the job.
For more information: Contact MSE3 Team.
Notes: Why it happened
Describe here the:
Immediate causes of the incident; and
Underlying causes of the incident
Lessons Learned: Four to five bullet points highlighting the main findings from the investigation. Remember the target audience is the front line staff so this should be written in simple terms in a way that everyone can understand.
Contract managers: Must review their risk assessment for this task capturing all points raised as a minimum and provide assurance to Contract Holders