## Slide 1
Date: 07.06.2020 Incident title HVL#11
What happened?
On June 7th, 2020 at 18:25hrs while tripping out 5”drill pipe. Drill pipe Stand was pulled and racked backed after rack back the AD pressed the float button to keep the link tilt in center position same time he used retract switch to bring it back link tilt faster. Once link tilt in center position AD started descending TDS. While lowering the TDS about 5meter below the monkey board, he unintentionally operated retract switch which resulted in the elevators and links hitting the horizontal beam in the mast at height of 20 meters and the links rested on the beam until the block is completely stopped.
Your learning from this incident..
Always ensure no distraction for Drillers/AD when operating the draw works.
Always Ensure Handovers to be done in a quiet environment where possible, stop the job if safe to do so.
Always ensure warning sign placed to ensure the break operator will not be engaged in any type of discussion while operating the brake (TDS).
Always engage with OEM in relation to update on critical equipment upgrades.
Always distribute learning to same type of rig.
Always position stabbing board camera to cover the mast during POOH.
Always maintain red zone while tripping and moving the block.
Never Distract Drawworks Operator while he is operating TDS
PDO Second Alert
Ensure the links are in float position when descending the blocks , do not operate the retract
Never Distract
Target Audience: Drilling, Operations, Logistics, Engineering & Construction
Notes: Ensure all dates and titles are input
A short description should be provided without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more!
Four to five bullet points highlighting the main findings from the investigation. Remember the target audience is the front line staff so this should be written in simple terms in a way that everyone can understand.
The strap line should be the main point you want to get across
The images should be self explanatory, what went wrong (if you create a reconstruction please ensure you do not put people at risk) and below how it should be done.

## Slide 2
As a learning from this incident and ensure continual improvement all contract
managers must review their HSE HEMP against the questions asked below
Confirm the following:
Do you ensure warning system is available to stop TDS if link tilt activated during descending?
Do you ensure your Rig Management (Toolpusher) intervein and address unsafe behavior and unsafe practices?
Do you ensure your TDS equipped with inter lock system and function appropriately?
Do you ensure there is a sign boards in place to remind others distraction to Drawworks operator?
Do you ensure for receiving updates and upgrades to the safety critical system from OEM?
* If the answer is NO to any of the above questions please ensure you take action to correct this finding.
Management self audit
Date: 07.06.2020 Incident title HVL#11
Notes: Ensure all dates and titles are input
Make a list of closed questions (only ‘yes’ or ‘no’ as an answer) to ask others if they have the same issues based on the management or HSE-MS failings or shortfalls identified in the investigation.
Imagine you have to audit other companies to see if they could have the same issues.
These questions should start with: Do you ensure…………………?