## Slide 1
Date: 12.11.2020 Incident title: HiPo#71
What happened?
On 12th November, the operation was rigging up of Client 3rd party sheave, after finishing TBT, derrickman was sent to monkey board to install the sheave on DC finger as per 3rd party JSA and previous job performed, at the same time the drill floor crew along with the third-party were preparing rig up of the sheave for installation. Once the sheave rigging was complete, the floorman was instructed by Driller to raise the sheave to monkey board level for installation by DM as agreed in the TBT. The plan was to hang the sheave on DC finger with the sling suspended from the hook. Derrick man was already present on monkey board when the sheave was lifted to the monkey board. DM assumes that the sheave is hanging with the winch line directly. Under the wrong impression DM opens the shackle and this results in the sheave come free and dropped to the rig floor. Weight of the sheave 22.9 kg fell from a height of 25mts.
Your learning from this incident..
Ensure effective TBT to be chaired by relevant third-party supervisor with (DSV, TP, 3rd party Supervisor) to be involved and cover all possible hazards present in the task.
Stop when you are in doubt. Do not perform the task without being clear on what is required.
Ensure procedure is followed and discussed. If changes are required, conduct risk assessment .
Ensure proper secondary retention to be available for the any equipment installed at height.
Ensure 3rd party companies have clear procedures on how to install and use their equipment.
Always Ensure the third - party premobilization process must be completed.
Ensure to hang the sheave on a certified hanging point ( not on monkey board fingers ) on the derrick.
Always Check and confirm the proper secondary retention in place for temporary equipment
PDO Second Alert
No provision for secondary retention of sheave and primary shekel removed
Sheave with independent securing
Target Audience: Drilling, Logistics & construction
Notes: Ensure all dates and titles are input
A short description should be provided without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more!
Four to five bullet points highlighting the main findings from the investigation. Remember the target audience is the front line staff so this should be written in simple terms in a way that everyone can understand.
The strap line should be the main point you want to get across
The images should be self explanatory, what went wrong (if you create a reconstruction please ensure you do not put people at risk) and below how it should be done.

## Slide 2
As a learning from this incident and ensure continual improvement all contract
managers must review their HSE HEMP against the questions asked below
Confirm the following:
Do you always ensure premobilization of the 3rd party is completed as per Company process?
Do you always ensure that rig supervisors get sufficient time to review 3rd party SOP and verify the equipment?
Do you always ensure that all third-party equipment's Drop object picture books verified at site?
Do you always ensure non-compliant third-party equipment reported?
Do you always ensure that the relevant JSA being used for execution of third-party tasks?
Do you always ensure third party are attending the TBT?
Do you always ensure sheave secondary retention is fitted?
* If the answer is NO to any of the above questions please ensure you take action to correct this finding.
Management self audit
Date: 12.11.2020 Incident title: HiPo#71
Notes: Ensure all dates and titles are input
Make a list of closed questions (only ‘yes’ or ‘no’ as an answer) to ask others if they have the same issues based on the management or HSE-MS failings or shortfalls identified in the investigation.
Imagine you have to audit other companies to see if they could have the same issues.
These questions should start with: Do you ensure…………………?