## Slide 1
Hands & Fingers Deep dive Q3 2023
Notes: Option I

## Slide 2
Q3 MSE3 Deep Dive Workshop
Incident number | Short Description | Incident Directorates | Contractor/Sub contractor
LTI#04 | Derrickman finger got crushed between the cap and cap liner resulted in finger amputation | UWD | SHALEEM
LTI#07 | AD’s hand got trapped between cellar pump and grating cellar resulted in a fracture | UWD | WEATHERFORD
LTI#11 | Roustabout hand got crashed between low torque valve and the ground | UWD | HALLIBURTON
LTI#12 | HVAC technician got a finger injury got while replacing the V belt. | UID | CARILLION
LTI#13 | AD's finger got caught & pinched while working pulling line for TDS | UWD | WEATHERFORD
LTI#16 | While aligning chisel with rock breaker housing, Mechanic finger was trapped between chisel and ground | DP | AL TURKI
The Deep dive was based on a theme related to Hands & Fingers incidents covering six LTIs:

## Slide 3: Insight
Hands & Fingers contributes more than 40% of recordable Injuries each year!!
Majorities of these injuries are related to pinch points/placing hands and fingers in the Line of Fire while doing the task.
Chart: 2023 TRCs by Categories
| Hands & Fingers | Slip, Trip & Fall | Released Energy | Others | Hit /Struck by | DROPs & Lifting | MVI | Burns
Total | 42 | 13 | 9 | 13 | 10 | 3 | 4 | 2
Chart: 2023 LTIs by Categories
| Hands & Fingers | Released Energy | Slip, Trip & Fall | Others | DROPs & Lifting
Total | 10 | 4 | 4 | 2 | 1
Chart: 2022 LTIs by Categories
| Released Energy | Hands & Fingers | Slip, Trip & Fall | DROPs & Lifting | MVI | Fire & Explosion | Others | Hit /Struck by
Total | 11 | 10 | 8 | 5 | 4 | 2 | 2 | 1
Chart: 2022 TRCs by Categories
| Hands & Fingers | Slip, Trip & Fall | Released Energy | Others | Hit /Struck by | DROPs & Lifting | MVI | Assault | Fire & Explosion
Total | 54 | 26 | 16 | 21 | 8 | 11 | 6 | 3 | 3

## Slide 4: Insight
DPM and UWD are the highest contributors (>70%) to Hands & Fingers injuries
Chart: 2023 Hands & Fingers TRCs by Diretorates
| DPM | UWD | UID | OSD | OND | GD
Total | 20 | 14 | 5 | 4 | 2 | 1
Chart: 2022 Hands & Fingers TRCs by Directorates
| DPM | UWD | UID | OND | UOD | GD | OSD
Total | 30 | 12 | 6 | 3 | 1 | 1 | 1

## Slide 5
Deep dive outcome patterns identified and causations:
2023 Q3 Incident Deep Dive
Chart: Immediate causations
| 3.1 Lack of knowledge of hazards present | 1.3 Violation (by supervisor) | 6.9 Improperly prepared tools | 6.2 Inadequate vehicle, plant for the purpose | 1.8 Improper lifting | 8.1 Congestion or restricted motion | 1.10 Shortcuts
 | 4 | 2 | 2 | 2 | 2 | 2 | 2
Chart: Deep dive outcomes
| Assurance | Communication | Training and development needs improvement | Drive for productivity shifts our risk tolerance | Risk Management | Safety Leadership | Procedures
 | 2 | 2 | 3 | 3 | 5 | 5 | 5
Chart: Underlying Causations
| 16.3 Inadequate identification of worksite/job hazards | 18.2 No/ inadequate risk assessment | 13.3 Inadequate identification of critical safe behaviors | 23.3 Inadequate communication between different organisations: | 18.3 Inadequate standard specifications and / or design criteria | 13.8 Employee perceived haste | 22.2 Inadequate development of PSP | 13.4 Inadequate reinforcement of critical safe behaviours | 22.4 Inadequate enforcement of Policy/Standard/Procedure (PSP) | 13.9 Habit / personal performance | 23.2 Inadequate vertical communication between supervisor and person | 13.2 Improper supervisory example | 11.1 Poor judgement | 19.1 Inadequate work planning or scheduling | 22.3 Inadequate implementation of PSP,due to deficiencies | 16.2 Inadequate leadership / supervision
Total | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3
Chart: MSF Causation
| 27.6 Inappropriate resource levels for supervision and management | 33.11 Inadequate assurance processes for implementation of management of change | 25.2 Inadequate implementation of systems for learning from incidents | 25.7 Inappropriate systems to ensure the quality or update of specifications or procedures | 29.2 Inadequate process implementation for STOP | 25.5 Inadequate processes and/or resource for quality check of HEMP | 31.3 Inadequate processes for management of change | 29.1 Inadequate focus on maintaining procedures up to date | 33.1 Inadequate Surveillance protocol for HSE standards | 29.13 Inappropriate process implementation for work with lifting equipment/ Lifting operations | 25.3 Inappropriate safeguards and management checks to avoid shortcuts/shortfalls
Total | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2

## Slide 6
2023 Hands & Fingers by Job Positions
Chart: 2023 Hands & Fingers TRCs by Job positions
| Technician | Helper | Derrickman | Floorman | Rigger | Roustabout | AD | Butcher | Welder | Pipe Fitter | Kitchen Boy | Instrument Fitter | Vehicle marshal | Steel Fixer | HGV Helper | Cable puller | AC Technician | Sand Blaster | Mechanical Technician | Cellar crew | Banksman | Chief Engineer | PMS Supervisor | Signaler | Electrician | Fabricator | Mechanic
Total | 4 | 4 | 4 | 4 | 3 | 3 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 2023 Hands & Fingers LTIs by Job positions
| Roustabout | AC Technician | PMS Supervisor | Mechanic | Derrickman | AD | Rigger | Floorman | Helper
Total | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 7
Safety Leadership | 
Incident number | Findings
LTI#04 | The NTP has experience in his current position, but he failed to comply with the SOP and failed to emphasize with the team the necessary safe work practice to change the Liner . The NTP and Assistant Driller were supervising the task, while the Floorman was collaborating with IP, but none of them intervened to stop the incorrect practice once IP placed his finger between Liner and Lock Screw.
LTI#07 | Improper supervision for the task while IP was directly contacting the pump whilst lifting in the presence of the Person in Charge (Junior Rig Manager).
LTI#11 | Supervisor was not supervising as he was participating in doing the task, not supervising as per JSA. This has been initiated as practice all the time and risk being normalized over the time. The team mainly used hands-free lifting straps for transporting or picking up boxes, but were not mandatory in the JSA for this activity.
LTI#12 | The PTW holder had been helping conduct the work (instead of limiting his role to supervising them) to help the team get the work done. HVAC manpower shortages in the contract at the time of the incident had led to increased pressure on the contract delivery and consolidation of teams (leading to two PTW holders in this one team). CALLC management did not effectively reiterate and reinforce the need for safety compliance over operational delivery, particularly when the reduced manpower situation increased the risk of instances of noncompliance.
2023 Q1 Incident Deep Dive
Examples of the findings with respective Patterns:
Risk Management & Communication | 
Incident number | Findings
LTI#04 | The site management failed to recognize the shortcut of changing the Liner. There was also inadequate monitoring of the job. The SOP and JHA had not been updated.
LTI#07 | Improper lifting technique in using the winch through the rotary table to lift the cellar pump , Crew were not aware of the correct way to remove the cellar pump. This was the first Rig move performed by this particular crew. Inadequate communication between organization and work group (Rigs). Other Ensign Rigs (148 and 149) completed over 50 Rig moves and the cellar pump was removed after the rig trailer leaves the well centre. Therefore, there is no communication between the work groups on the right way to remove the cellar pump. In addition, it was the first rig move the crew did since the start of Rig 150 operations. .
LTI#11 | A combined work when it comes to third parties involved in the job, each company uses their internal JSA . It has been identified that there is no combined JSA between parties involved to the job that facilitate and generate clear roles and responsibilities. This lack of control over JSA’s, between the two organizations, increased the likelihood of hazards being identified and effectively controlled, including the availability and use of ‘hands free’ equipment.
LTI#12 | The management process for conducting risk assessments and developing method statements in CALLC has been ineffective as it historically did not require to include the people at risk to utilize their experience and knowledge.

## Slide 8
2023 Q1 Incident Deep Dive
Training and development | 
Incident number | Findings
LTI#12 | There had been an over reliance on trade qualifications to prove competency. The last internal CALLC training/competency assessment on HVAC was in 2014 prior to the Coriolis competency assessment in 2023.
LTI#16 | Management failed to conduct thorough assessments to determine appropriate resource levels, leadership development and training programs to equip competent supervisors with the skills needed to effectively supervise and lead their teams.
Procedure | 
Incident number | Findings
LTI#04 | There is no mechanism for routinely reviewing Procedures during the site visit by management. Management failed to carry out a quality review during last visit.
LTI#07 | Cellar Pump removal was not included in the Rig Move SOP and JSA as it was not included in the management system.
LTI#11 | JSA that was used was found with many critical steps missing, not up to date as it has been used old version available on computer . Directional driller did not initiate the Document controlled version of the JSA for GEO SPAN assembly as connectivity was very slow and was unaware on how to pull the latest version from the system. Halliburton JSA’s are accessible through a Network system, hence, when the connectivity is slow, some people default to using the latest available JSA saved ones in their laptops. The issue being it may be an outdated JSA not including any newly identified risks.
LTI#12 | The CALLC method statement for the HVAC maintenance did not include the requirement to loosen the belt tension as the risk assessment had not identified the risk. The risk assessment had been conducted without involving those doing the work and facing the safety risk.

## Slide 9
2023 Q1 Incident Deep Dive
Assurance & Compliance | 
Incident number | Findings
LTI#04 | While self-verification from the previous visit was completed, it was insufficient to identify that the steps is not in compliance with Standard Operating Procedure (SOP) during changing the Piston and Liner. There was also inadequate monitoring of the job.
LTI#13 | No audits, reviews of the successful implementation and use of the management of change process
LTI#16 | ATE Management system failed to identify the shortfalls in the maintenance area by conducting routine audits and inspections to ensure that the use of right equipment for the tasks are in place and being followed correctly. No specific audits are planned for assuring compliance to industrial safe practices in the vehicle / plant maintenance activities.

## Slide 10
What next
Below are program in place from UWD & DPM to address the Hands & Fingers:
UWD | DPM
Hands & Fingers injuries prevention Campaign : - All units shall have a pinch point register which identifies all potential pinch points on location and the controls needed to prevent pinch point injuries. - Fit for purpose hands off tools (push pull sticks, finger savers etc.) are made available at site and the crew trained to use these tools. - The gloves used for the activities shall be fit for purpose - A matrix for the type of gloves/hands off tools w.r.t the activity should be available as part of the contractor hand and finger injury prevention program - Hands & Fingers Questionnaires in TBT/Mustaed - Hands & Fingers videos : Issa Story etc. | Procedures & Risk management: To update & review HEMP related to hands & fingers. Safety leadership: Continuous delivering FLS adding a slide related to hands & fingers. Training & development: Ensuring all supervisors attended FLS. Communication: Ensure all incidents related to hands & fingers are communicated to all levels at site. Assurance: Adding in TBT pinch points element to ensure workers pre-inspection conducted.

## Slide 11: Patterns and their definition
Drive for productivity shifts our risk tolerance | A positive drive for productivity, production targets, that creates an unintended consequence of the drive for productivity can be a willingness to accept conditions or behaviours with more risk (i.e., shift the risk tolerance). Higher risk tolerance can become the new norm over time.
Training and development needs improvement | Deficiencies in the systems for providing the necessary knowledge or skills, no training provided.
Error enforcing conditions | Factor such as time pressure, changes in work patterns, physical working conditions (hot, cold, noisy etc.) that promote human errors.. These include things like activity overload, vacancies in critical areas, resources without adequate training and development, contracts not working, organisational initiatives. We sometimes fail to recognise the potential cumulative impact of these conditions.
Assurance | Deficiency or lack of assurance process
Procedures | Unavailable, Unclear, incorrect or otherwise ineffective work instructions.
Maintenance | Failure in the system for ensuring technical integrity of facilities, plant, equipment and tools.
Design | Deficiencies in layout or design of facilities, plant or equipment.
Communication | Failure in effectively transmitting information. ( In affective TBT and Risk Management , not sharing procedure)
Failed to effectively implement learning from incidents | Not been able to effectively embed and sustain learning from incidents, not actively looking for opportunities to learn from incidents. not had the time and resources for investigations to go deep enough. The focus tends to be on the technical aspects of the incidents with less time spent investigating the human behavioural aspects. Actions are to address the more obvious failures rather than the deep-seated underlying problems.

## Slide 12: Repeated incident used criteria
Same Top Event
Same Immediate Cause
Same underlaying cause / Management system failure
Same company
An incident is considered as repeat if at least three out of the below criteria have been met:

## Slide 13: Safety Refresh
Safety Leadership
Contractor HSE Management
Road Safety
Risk Management Learner Organization Process Safety