## Slide 1: Learning From Incident - First Alert
What happened:
PIM # | 1173445 | Date & Time | 27.12.2024, 03:30am | Location | Hoist 54 Marmul
Incident Type | LTI#26 | Category | DROPs | Activity | Rig down Rig Floor
Target Audience: Rig Manager, Night Toolpusher, Driller, AD, Derrickman, Floorman
In case of an emergency please call PDO Emergency Number (Toll Free): 2467-5555
Prevent
Initial Findings:
Always stay away from line of fire during R/D rig Floor
The floorman was standing at A frame of the mast (in the LoF) during rig down work, instead of standing at the driller panel.
Rig floor dropped item (frame) was not secured with safety pin.
The safety pin (of the frame) was not part of ‘Drops inspection checklist’.
AD was not supervised by NTP during the R/D work floor.
How do you ensure that you are standing away from line of fire (LoF) when removing safety pin during R/D work Floor ?
How do you ensure that potential drop hazards are identified, and secondary retention are installed?
How do you ensure employees are aware about Hazard and risk of potential dropped objects and LoF?
How do you ensure effective supervision is available during the task?
Engagement Questions:
At approximately 03:24 hours, during R/D at the rig floor, the crew raised the rig floor to a vertical position, one of a small section of the rig floor dropped from its original position and struck the floor man's left foot, who was standing on the mast frame to remove the safety pin. This resulted to fracture of the left foot.
Dropped frame was not secured with safety pin
Right position while removing pin
Notes: Mr Musleh image on the top right will change according to incident pattern, MSE3 will provide you with the image as per the pattern
What happened: A short description should be provided without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more!
Initial Finding: Four to five bullet points highlighting the initial main findings from the investigation. Remember the target audience is the front-line staff so this should be written in simple terms in a way that everyone can understand.
Learnings: Four to five learning message in the form of questionnaires linked with initial findings
The strap line should be the main learning point you want to get across
The images should be self explanatory, what went wrong (if you create a reconstruction please ensure you do not put people at risk) and below how it should be done.