## Slide 1
What happened?
On May 9, 2023, at 01:10 a.m. After the mast up, The Derrickman noticed the sand line lose & drawn towards the drawworks side; he acted to pull the line so that it starts sliding towards mast, instead the line started retracting towards drawworks side; The Derrickman rushed down the mast carrier stairs & in doing so missed last 02 steps on the carrier stairs while jumping to the ground, landing on uneven ground with few stones which caused ankle sprain.
Why it happened/Finding:
PTW, JHA, and TRIC were all in place. Slip trip & fall hazards were discussed. Mast up SOP does not mention securing of the sand line in place.
Night tool pusher was not supervising the critical activity.
The Musta’ed numbers 3 and 2 were not followed, the access and aggress for the emergency were not identified, and the stored energy wasn't considered during risk assessment.
When the derrickman noticed the sand line retracting towards draw works, he rushed to escape the line of fire, missed few stairs steps and jumped to the ground.
When using stairs, the Derrickman failed to make a three-point contact.
The Stairs design was noncompliant to PDO SP 2215 – 3 recommendations.
Your learning from this incident..
Always ensure to secure loose lines on both side of mast before mast up or down to arrest any unplanned movement.
Always ensure that all the stair steps have width & height of at least 9.5” & the angle to platform not more than 50 degrees.
Always ensure to maintain three points of contact while using stairs.
Always ensure to maintain housekeeping & that landing area of stairs is levelled.
Always ensure that safe work practices are followed and that your physical position is clear of line of fire.
Always make sure that the pre-tour meeting is conducted taking into consideration all 7 elements of Musta'ed verification.
Always ensure that unsafe acts and conditions are stopped and intervened.
Date 09/05/2023 Incident title: LTI#03 Ankle injury descending stairs Pattern: Slips, Trips, Falls Potential severity: B3P
Target Audience: Drilling, Logistics, Operation & Construction
PDO Second Alert
Always maintain three-points of contact & avoid rushing while ascending or descending stairs
Notes: Ensure all dates and titles are input
A short descrDerrickmantion should be provided without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more!
Four to five bullet points highlighting the main findings from the investigation. Remember the target audience is the front line staff so this should be written in simple terms in a way that everyone can understand.
The strap line should be the main point you want to get across
The images should be self explanatory, what went wrong (if you create a reconstruction please ensure you do not put people at risk) and below how it should be done.

## Slide 2: Management self audit
As a learning from this incident and ensure continual improvement all contract managers must review their HSE risk management against the questions asked below
Confirm the following:
Do you have regular verifications conducted to check if the area of access and egress are clear of any hazards?
Do you always ensure that the self verification audits & assurance plans cover the design verifications of the stairs?
Do you ensure that HSE Assurance audits have been performed for compliance verifications on the unit regularly?
Do you have the 3-point contact rule for stairs as part of HSE Induction?
Do you ensure that the toolbox talk carried out is in accordance with Musta’ed 7 elements verifications?
Do you always ensure that the crew understand & discuss the Line Of Fire during the toolbox talk?
* If the answer is NO to any of the above questions please ensure you take action to correct this finding
Date 09/05/2023 Incident title: LTI#03 Ankle injury descending stairs Pattern: Slips, Trips, Falls Potential severity: B3P
Disclaimer
This document is provided for information only. It may not be relied upon for any purpose. Neither PDO nor any party providing information for this document accepts any liability for its accuracy, completeness, omissions, advice, or any consequences arising from its use, even if reasonable care was not exercised. No representation or warranty, express or implied, is made that following this document will achieve any specific results or meet any legal or regulatory requirements. This document does not constitute technical advice; consult a qualified professional if such advice is needed
Notes: Ensure all dates and titles are input
Make a list of closed questions (only ‘yes’ or ‘no’ as an answer) to ask others if they have the same issues based on the management or HSE-MS failings or shortfalls identified in the investigation.
Imagine you have to audit other companies to see if they could have the same issues.
These questions should start with: Do you ensure…………………?