## Slide 1
What happened?
The Forklift Operator needed to switch the fork for a boom attachment to complete a task but couldn’t remove the fork because the connecting bolt between the Forklift Pin and the Hydraulic piston had broken. As a result, the Forklift Pin became disconnected from the Hydraulic piston. Additionally, a fragment of the broken bolt became lodged within the Forklift Pin, causing it to jam inside the frame. The Forklift Operator reported this issue to the Chief Mechanic, who inspected the Forklift and asked the Forklift Operator to wait, as the Chief Mechanic was busy with the generator.
Despite the Chief Mechanics instruction to wait, the Forklift Operator and the Welder (Sub-contractor) agreed to remove the pin from the Forklift frame. The Welder placed an external bolt inside the Forklift frame so that he could use hammer to drive the pin outside of the Forklift frame.
As the Welder inserted the external bolt inside the frame, the Hydraulic Piston was engaged by the Forklift Operator and the Welder's right hand got trapped between the bolt and the Forklift frame. This resulted in a crush injury to his right thumb and index finger.
The Welder was first taken to the Rig Clinic for initial treatment and then transferred to Nizwa Hospital, where he underwent hand surgery.
Why it happened/Finding :
Performing activities without authorization.
Inadequate planning, poor communication and no risk management carried out.
Inadequate enforcement of procedure and processes that led personnel do things their own way.
Lack of knowledge on Hazard ID and Risk Management.
Inadequate management of callout sub-contractor (welder) personnel.
The preventative maintenance checks did not specify to check bolt conditions.
Your learning from this incident:
Ensure everybody stops the activity when they are told to do so.
Ensure all employees / subcontractors are effectively engaged in Hazard ID and Risk Management process,
Ensure there is an effective two-way communication with employees, sub-contractors that safety is a top priority.
PM checks to set criteria, frequency to inspect and replace bolts.
Encourage employees to challenge and report rule breaks, to grow a positive health and safety culture within workplace.
Date:27 Dec 2024 Incident title: LTI# 27 Pattern: Hands and Fingers. Potential severity: B4P Activity: Non-routine
Target Audience: Forklift operator and Mechanic
PDO Second Alert
Ensure work authorization and correct hand placement.
Notes: Ensure all dates and titles are input
A short description should be provided without mentioning names of contractors or individuals. You should include, what happened, to who (by job title) and what injuries this resulted in. Nothing more!
Four to five bullet points highlighting the main findings from the investigation. Remember the target audience is the front line staff so this should be written in simple terms in a way that everyone can understand.
The strap line should be the main point you want to get across
The images should be self explanatory, what went wrong (if you create a reconstruction please ensure you do not put people at risk) and below how it should be done.

## Slide 2: Effective Learning
To make sure learning is translated to the site day to day activities , please answer the below questions :-
How learning can be implemented at site ?
Ensure that everyone stops their activities when instructed and refrains from performing any tasks without proper authorization.
Implement control measures to facilitate effective communication, taking language barriers into account.
Conduct a survey on subcontracted equipment to verify that all moving parts, connections, etc., are included in the preventive maintenance program.
How can you sustain the action ?
Implement a competency framework for subcontracted personnel.
Actions learned from the incident shall be incorporated into the management self-verification program.
Date:27 Dec 2024 Incident title: LTI# 27 Pattern: Hands and Fingers. Potential severity: B4P Activity: Non-routine
Disclaimer
This document is provided for information only. It may not be relied upon for any purpose. Neither PDO nor any party providing information for this document accepts any liability for its accuracy, completeness, omissions, advice, or any consequences arising from its use, even if reasonable care was not exercised. No representation or warranty, express or implied, is made that following this document will achieve any specific results or meet any legal or regulatory requirements. This document does not constitute technical advice; consult a qualified professional if such advice is needed
Notes: Guideline for Effective Learning & Sustainability
•Can be replicated across similar contractor / activities
•Shall be SMART- Specific ,Measurable , Achievable ,Realistic & Timebound
•Can be implemented in a months' time